## Slide 1
Airway Surface Liquid (ASL) heights
Area between mucus and epithelial cells
One of the many approaches in measuring the effects of peptides
A single experiment can yield thousands of images
Can be very subjective

## Slide 3
Considerations
Processing images in their entirety is computationally expensive
  This needs to be ran by a researcher that does not access an HPC cluster, cloud, etc
Can be complicated, so should try to employ machine learning
  But as above, must be lightweight
Needs to be comparable to historical data
  Benchmark the software against old data

## Slide 4
Make some categories
Have researchers rate images on a spectrum
  Allows for a form of leniency to make a pass/fail call
1
3
2
5

## Slide 5
Find the data
What features do great/good images have over bad/unusable images?
  All lies in the distribution of signal
  Isolate red channel, sum intensities
  Serves as a more lightweight alternative to and entire image
  Use these distributions to train a random forest
file group distribution
✔ IMG01 1 0000000000011115559999555111100000000000
❌ IMG02 5 9999999999988887777666222110000000000000
✔ IMG03 1 0000000000000000000000000002234889876510
✔ IMG04 1 0000112255889996521000000000000000000000
✔ IMG05 2 0000000000000000033888844221100000000000

## Slide 6
Measuring ASLs of passing images
If an image passes, the distribution is fit to a high order polynomial
  Allows for ‘flexing’ across the data to find a ‘peak’
Highest peak with the neighboring valleys allow to pinpoint the band
Capturing the band width itself is relatively easy

## Slide 7
Results
Training model allows for 96% accuracy in classifying images as pass or fail
  Losing a good image isn’t the end of the world
  Keeping a bad image is, so reporting IQR of data protects the confidence of results
High speed
  ~300/min on cheap computer
Automated output
  ggplots, Excel compatible tables
  Groupwise comparisons
  Pass/fail PDF and log for review